## Slide 1
eSPAARO 5 Spektrum Transmitter Layout
Right Stick
Ch. 1: ← → dlat: [-1,1]
Ch. 2: ↕ dlon: [-1,1]
1
-1
1
-1
1
-1
1
-1
Left Stick
Ch. 4: ← → ddir: [-1,1]
Ch. 3: ↕ dacc: [-1,1]
Legend
--- RcChannel Channel Number
--- Spektrum Switch Label
A | Ch. 5 | RTL
↑ 0 = Nominal
↓ 1 = RTL
H | Ch. 8 | PTI Arm
↑ 0 = Nominal
↓ 1 = Engage
B | Ch. 6 | Flt Mode
↑ 0 = Altitude
━ 1 = Stabilized
↓ 2 = Manual
R Knob | Ch. 9 | PTI Amp
↑ = 1
↓ = 0
G | Ch. 10 | Engage Fault
↑ 0 = Fault.
━ 1 = Nominal
↓ 2 = Nominal
C | Ch. 6
Ctrl Mode
↑ 0 = Stock
━ 1 = Custom
↓ 2 = Custom
D | Ch. 7
Flt Mode
↑ 0 = Position
━ 1 = Altitude
↓ 2 = Stabilized
D2 | Ch. 7
Arm
↑ 0 = Arm
↓ 1 = Disarm
L Slider | Ch. 5
Brake
↑ 1 = No brake
↓ 0 = Brake
R Slider | Ch. ?
Unassigned
↑ = Text 1
━ = Text 2
↓ = Text 3
E2 | Ch. ?
Unassigned
↑ 0 = Text 1
━ 1 = Text 2
↓ 2 = Text 3
E | Ch. 12
Mod 1: CA Mode
↑ 0 = Exp.
━ 1 = Stock
↓ 2 = Stock
F | Ch. 11 | PTI Mode
Mod 2
↑ 0 = Multisine
━ 1 = Freq. Sweep
↓ 2 = Doublet